## Slide 1: Drive Trains
The Bionic Tigers - 10464

## Slide 2: Considerations when choosing
Speed
  How fast do you want to go?
Power
Maneuverability
Traction
Terrain
Omni-directional

## Slide 3
4 Wheel
6 Wheel
Mecanum
X-Drive
H-Drive
Treads
Swerve Drive
Drivetrain Types
The most common drivetrain configurations in FTC

## Slide 4
4 Wheel
4 Traction Wheels
  Good Traction
  Poor Maneuverability
2 Traction 2 Omni
  Off-Center Rotation
  Good traction
  Good Maneuverability
4 Omni Wheels
  Good Maneuverability
  Poor Traction
4 Traction
2 Traction
2 omni
4 omni

## Slide 5
6 Wheel
High Traction
Good Maneuverability
Versatile Terrain
Can’t strafe
4 omni 2 traction

## Slide 6
Mecanum
High Maneuverability
Good Traction
Strafing
Best on flat field
Requires exact measurements for best application

## Slide 7
X-Drive
High Maneuverability
Poor Traction
Strafing
Unorthodox Motor Placement
Static Buildup

## Slide 8
H-Drive
High maneuverability
Strafing
Poor traction
Space and motor consuming
Static Buildup

## Slide 9
Treads
Good traction
Versatile Terrain
Poor maneuverability
Prone to breaking

## Slide 10
Swerve
High maneuverability
Good traction
Complex programming
Space consuming
Complex design

## Slide 11
Drive Methods
How to get from motor to wheel
Direct Drive
Chain Drive
Belt Drive
Gear Drive

## Slide 12
Direct Drive
Motor and wheel share the same shaft
Fewer points of failure
No flexibility in motor position
Wears down motor gearbox

## Slide 13
Chain Drive
Flexible motor positioning
Variable gear ratio
Adjustable length
Requires tension
Multiple points of failure

## Slide 14
Belt Drive
Flexible motor position
Low maintenance
Variable gear ratio
Relatively few points of failure
Requires precise positioning
Requires tension

## Slide 15
Gear Drive
Semi-flexible motor position
Variable gear ratio
Can slip and grind
Multiple points of failure

## Slide 16: Tips and Tricks
Advice based on our own learnings
Take advantage of D shaped and hex shafts
Use consistent structure such as channel pieces
CAD and prototype before making complicated assemblies
Plan your drivetrain to accommodate the other mechanisms on your robot

## Slide 17
Credits
This lesson was written by The Bionic Tigers 10464 for FTCTutorials.com
You can contact the author at
More lessons for FIRST Tech Challenge are available at www.FTCtutorials.com
Copyright 2020 FTCTutorials.com (Last edit 4/1/2020)
This work is licensed under a
Creative Commons Attribution-NonCommercial-ShareAlike 4.0 International License.
Website:
  http://lovelandrobotics.com/team10464
Twitter:
  @BionicTigersFTC
Email:
  BionicTigers10464@gmail.com