## Slide 1: Drive Trains
The Bionic Tigers - 10464

## Slide 2: Considerations when choosing
Speed
  How fast do you want to go?
Power
Maneuverability
Traction
Terrain
Omni-directional

## Slide 3: Drivetrain Types
4 Wheel
6 Wheel
Mecanum
X-Drive
H-Drive
Treads
Swerve Drive

## Slide 4: 4 Wheel
4 Traction Wheels
  Good Traction
  Poor Maneuverability
2 Traction 2 Omni
  Off-Center Rotation
  Good traction
  Good Maneuverability
4 Omni Wheels
  Good Maneuverability
  Poor Traction
4 Traction
2 Traction
2 omni
4 omni

## Slide 5: 6 Wheel
High Traction
Good Maneuverability
Versatile Terrain
Can’t strafe
4 omni 2 traction

## Slide 6: Mecanum
High Maneuverability
Good Traction
Strafing
Best on flat field
Requires exact measurements for best application

## Slide 7: X-Drive
High Maneuverability
Poor Traction
Strafing
Unorthodox Motor Placement
Static Buildup

## Slide 8: H-Drive
High maneuverability
Strafing
Poor traction
Space and motor consuming
Static Buildup

## Slide 9: Treads
Good traction
Versatile Terrain
Poor maneuverability
Prone to breaking

## Slide 10: Swerve
High maneuverability
Good traction
Complex programming
Space consuming
Complex design

## Slide 11: Drive Methods
How to get from motor to wheel
Direct Drive
Chain Drive
Belt Drive
Gear Drive

## Slide 12: Direct Drive
Motor and wheel share the same shaft
Fewer points of failure
No flexibility in motor position
Wears down motor gearbox

## Slide 13
Chain Drive
Flexible motor positioning
Variable gear ratio
Adjustable length
Requires tension
Multiple points of failure

## Slide 14: Chain Drive
Flexible motor positioning
Variable gear ratio
Adjustable length
Requires tension
Multiple points of failure

## Slide 15: Belt Drive
Flexible motor position
Low maintenance
Variable gear ratio
Relatively few points of failure
Requires precise positioning
Requires tension

## Slide 16: Gear Drive
Semi-flexible motor position
Variable gear ratio
Can slip and grind
Multiple points of failure

## Slide 17: Tips and Tricks
Advice based on our own learnings
Take advantage of D shaped and hex shafts
Use consistent structure such as channel pieces
CAD and prototype before making complicated assemblies
Plan your drivetrain to accommodate the other mechanisms on your robot

## Slide 18: Credits
This lesson was written by The Bionic Tigers 10464 for FTCTutorials.com
You can contact the author at:
  Website:
    http://lovelandrobotics.com/team10464
  Twitter:
    @BionicTigersFTC
  Email:
    BionicTigers10464@gmail.com
More lessons for FIRST Tech Challenge are available at www.FTCtutorials.com
This work is licensed under a
Creative Commons Attribution-NonCommercial-ShareAlike 4.0 International License.