## Slide 1: Initial Robot Configuration
Team 13380
QUANTUM STINGERS

## Slide 2: The Phones

## Slide 3: Phones for FTC
For FTC, every team/robot needs two Android phones
Starting with the 2020-2021 FTC Season, only Motorola Phones will be allowed (see a specific list in FTC Game Manual 1, page 33)
Two phones:
  Driver Station Phone (DS)
    Used by drivers/coach during robot game to start autonomous, etc.
  Robot Controller Phone (RC)
    Stays on robot, connected to Rev Hub (an alternative to this phone is using the Rev Control Hub)

## Slide 4: Setting Up the Phones
Steps to Setting Up
  Rename the phone using the following format: “Team# - DS” for Driver Station and “Team# - RC” for Robot Controller
    You can do this by going to Settings → Wifi → Advanced Wifi→ Wifi Direct → Configure Device
  Install the FTC Driver Station App on the DS phone, which can be found through the Google Play Store, on the Driver Station Phone.
  Similarly install the FTC Robot Controller App on the RC phone
For the next step, Pairing, make sure both phones are in Airplane mode but still keep the Wifi on

## Slide 5: Pairing the Phones
Pairing the DS and RC phones will allow flow of telemetry data between phones, gamepad input, and selection of operation modes.
Steps to Pairing:
  Verify that Robot Status is “Running” on the Robot Controller App on the RC phone
  On the DS phone, launch the pairing: go to Driver Station App → the triple-dot pop-up menu → Settings → Pairing Method → Wifi Direct
  Still under Settings → Pair with Robot Controller; then find and select your RC phone in the options (the name that you initially set the phone to should show up; if it doesn’t, check the wifi for the phones)
  On the RC phone, accept the pairing in the Robot Controller App
This is how the DS app should look like →
This is how the RC app should ← look like

## Slide 6: Rev Expansion Hub:

## Slide 7: What is the Rev Expansion Hub?
A Rev Expansion Hub is the FIRST-approved control hub/port.
It is a hardware controller and interface that communicates between all the robot’s motors, servos, sensors, battery, robot switch, and the Robot Controller phone.
It has various external ports that are used to make these connections
The robot can have a maximum of 2 Rev Expansion Hubs

## Slide 8: Rev Hub External Ports
Switch/ Battery→
Motors/ Encoders→
Servos^
← Color/Distance Sensor
← Touch Sensor
RS485
UART
12C
DIGITAL
Analog
^Mini USB Port (for phone)
XT30 Power ← Port
← Hub to Hub
Connection

## Slide 9: Making Connections
Rev Hub to RC Phone
    USB Type A male to type B-mini male cable
    Micro USB OTG adapter
  Connect the USB type B-mini end to the Mini USB port on Rev Hub
  Plug in the Type A end into the OTG adapter
  Plug in the adapter to the RC phone
Rev Hub to the Battery/Switch
    Rev Switch
    Rev Tamiya to XT30 Adapter
    12V Battery
  Connect one of the Switch cables to the Adapter
  Connect the Tamiya Adapter to that of the Battery
  Connect the other end of the Switch to the top left battery port on the Rev Hub, as shown

## Slide 10: Connections Continued...
Rev Hub to DC Motors
    Anderson Powerpole to JST VH Adapter
  Most of the DC motors should already have an Anderson Powerpole connector
  Connect the motor’s Anderson Powerpole to that of the adapter
  Plug in the Adapter to a Motor Port on the left side of the Expansion Hub, under the battery/switch
  Encoders are plugged in to the small port directly next to where the corresponding motor is plugged into
Rev Hub to Servos
  Just connect the 3-wire connector of the Servo to one of the Servo Ports at the bottom of the Rev Hub
Rev Hub to Sensors
  Color Distance Sensors have 4-wire connectors that plug into the Ports labeled “12C” on the right side of the Rev Hub
  Touch Sensors have 4-wire connectors that plug into the Ports labeled “Digital” on the right side of the Rev Hub
Anderson Powerpole →
JST VH→
A full layout:
Servo:
Motor →
← Encoder

## Slide 11: Rev Hub to Rev Hub Connection
One Rev Expansion Hub has 4 motor and 6 servo ports
For teams that use two Rev Hubs to accommodate for all the robot hardware, both Rev Hubs must be connected. Only one of the Rev Hubs will be connected to the RC phone.
Part 1
  By default, all Rev Hubs have an equal, predefined serial address (2)
  In order to connect two Rev Hubs, their addresses must be different, so one of them needs to be reconfigured
    Connect one Rev Hub to the Robot Controller Phone and the Switch/Battery
    Open RC App
    Create a temporary configuration file
    Go to Settings → Advanced Settings→ Expansion Hub Address Change
    Now, change the current address from 2 to another value
    Click Done
    Delete the Temporary configuration file and create a new, permanent one

## Slide 12: Rev Hub to Rev Hub Connection
Part 2: Wire Connections
    Disconnect Rev Hub from phone and Battery/Switch
    Use a XT30 Extension Cable → Plug into the XT30 Power ports of both Rev Hubs
    Use a 3-pin JST PH Cable → Plug into RS485 Ports of both Rev Hubs
    Connect one of the Rev Hubs to the RC Phone, and the other Rev Hub to the Switch/Battery
    Make sure that both of these connections are made with only 1 continuous wire each (no extensions)
This is how it should look:
← JST Cable
XT30 Ext.

## Slide 13: Robot Configuration

## Slide 14: What is Robot Configuration?
To communicate with any motors, servos, or sensors wired to the Rev Hub’s external ports, you must configure them in your Robot Controller Phone
Configuration is based off of which hardware parts are connected to which Rev Hub Port
  Every external port on the Rev Hub has a label (ex. Motor Port 1 or RS485 Port 2, etc.) This label is used to identify how the hardware is connected to the Rev Hub
  The hardware parts (motors, servos, sensors) should also be named (ex. Back_Left_Motor); this name should be consistent with your code
Configuration is done on the Robot Controller Phone
The Phone must be physically connected to the Rev Expansion Hub(s)
The robot must be configured in order to run any programs

## Slide 15: Steps to Configuration
Steps to Configuration:
  Physically connect RC phone to the Rev Hub
  Go to the Robot Controller App
  Click on triple-dot for the drop down menu
  Click “Configure Robot”
  For the first-ever Configuration
    Click New
    Click Scan to find all connected Rev Hubs
  Click on the Rev Hub that you want to configure
  Now you should be able to a list of ports
  Click on the one you want to configure (ex. motors)
  Now you will see a list of ports (0,1,2,3...)
  Under the corresponding port, click the drop-down menu and select the correct robot part type
  Make sure that your configuration matches the actual connections on the Rev Hub
    For example, if Back_Left_Motor is plugged into Motors Port 0 of Rev Hub1, type “Back_Left_Motor” in Rev Expansion Hub Portal 1 → Motors → Port 0
  After configuring all hardware parts, click Done → Save

## Slide 16: Steps to Configuration:

## Slide 17: Credits
This lesson was written by Vennela Jonnala of Team 13380 (Quantum Stingers) for FTCTutorials.com
You can contact the author at vennelashriya@gmail.com
More lessons for FIRST Tech Challenge are available at www.FTCtutorials.com
This work is licensed under a
Creative Commons Attribution-NonCommercial-ShareAlike 4.0 International License.